## Slide 1
CLIC Module
and
X-band RF components
Alexandre.Samochkine @ cern.ch

## Slide 2: CONTENT
CLIC LAYOUT
CLIC MODULE
  - LAB version
  - CLEX version
RF COMPONENTS
  - Accelerating Structure
  - Power Extraction and Transfer Structure
  - PETS “On-Off” mechanism
  - Choke Mode Flange
  - Hybrid
  - Splitter
  - RF Compact Load
  - 60 db Directional Coupler
  - Compact RF Pumping Port
  - RF Vacuum Gate Valve

## Slide 3: OVERALL CLIC LAYOUT ( 3 TeV )
Main Beam Generation Complex
Drive Beam Generation Complex
Main LINAC
x 2 = 21452 Two-Beam Modules

## Slide 4: CLIC project time-line *
* S. Stapnes, CLIC Workshop 2013, CERN

## Slide 5: RF UNIT
3D model
Schematic view
Each PETS * feeds 2 AS **
P ower
E xtraction &
T ransfer
S tructure
*
A ccelerating
S tructure
**

## Slide 6: CLIC MODULE LAYOUT
n RF units + magnets + vac. syst. + alignment syst. + stabilization syst. form the Module (L = 2010 mm)
CLIC at 500 GeV  26’950 Accelerating Structures, 13’475 PETS, ~ 80’000 RF components
CLIC at 3 TeV  143’072 Accelerating Structures, 71’536 PETS, ~ 400’000 RF components

## Slide 7: ACCELERATING STRUCTURE
… is the most complex and precise component

## Slide 8: AS CELL
… the tolerances required to satisfy the RF and beam dynamic constraints
Cell shape accuracy:
  zone A - 0.005 mm
  zone B - 0.02 mm
Flatness - 0.001 mm
Surface roughness:
  zone A Ra 0.025 μm
  zone B Ra 0.1 μm
regular cell
ZONE A
ZONE B
DRAWING

## Slide 9: Super AS assembly
a number of bonding and brazing cycles needed

## Slide 10
Second prototype: under engineering design
Optimised geometry (less material);
Bonding test.
First prototype: under test at CERN
Machining test;
Bonding test.
Vacuum manifolds are brazed to the bonded disk stack
- many pieces to handle;
- potential assembly errors;
- risk of braze filler material inside the structure;
- additional features (e.g. cooling circuits).
Several heating cycles;
High cost.
Launched the study of integrated disk (integrate several function as one piece).

## Slide 11: PETS
… made of joint octants placed in a mini-tank brazed to a compact coupler combined with ‘ON-OFF’ mechanism
P ower
E xtraction &
T ransfer
S tructure

## Slide 12: PETS bar (octant)
Double-length PETS bar for CLEX tests
Octant shape accuracy - 0.015 mm
Flatness - 0.01 mm
Surface roughness - Ra 0.1 μm
DRAWING

## Slide 13: PETS UNIT ASSEMBLY
brazing and EBW steps required
Pre-alignment
& control
Assembled unit

## Slide 14: MODULE PROTOTYPE TEST PROGRAM
LAB version (no RF)  4 modules
Demonstration of the two-beam module design (from single technical system to complete modules)
This implies the assembly and integration of all components and technical systems, such as RF, magnet, vacuum, alignment and stabilization, in the very compact 2-m long two-beam module
2010 - 2017
Demonstration of the two-beam acceleration with beam and RF with real modules
Address other feasibility issues in an integrated approach
CLEX version (beam, RF) 3 modules
NEEDS 2013-2017
2013
20 AS, 10 PETS
2014
24 AS, 12 PETS
2015
32 AS, 16 PETS
2016
32 AS, 16 PETS
2017
32 AS, 16 PETS

## Slide 15: PREPARATION AND MODULE ASSEMBLY ( LAB )
8 AS ready for installation
RF network
PETS fixed on the Drive Beam girder
First fitting of the first Super-AS

## Slide 16: LAB TESTS
the first LAB Module (assembled at the end of 2012) is currently under thermal tests

## Slide 17: CTF3 (CLEX)
DELAY LOOP
COMBINER RING
CHICANE
LINAC
TWO-BEAM
LINE
CALIFES
Probe Beam
Injector
INJECTOR
C LIC
T est
F acility
AS tank
PETS tank
CLEX
CLEX -
CLIC EXperimetal area
TBTS
T wo
B eam
T est
S tand

## Slide 18: PROTOTYPE MODULES IN CLEX
– 2017
2014 –
3D model. Integration of
the first CLIC Module in CLEX (Jun’13)
end 2013
CLEX Module Type 0
CLEX -
CLIC EXperimetal area
3 modules

## Slide 19: PETS “On-Off” mechanism
Reflector
The breakdowns happen from time to time either in AS or PETS. In order to maintain the overall luminosity of the machine it is necessary to terminate the RF power locally almost immediately (within 18 ms) after breakdown and engage it gradually afterwards so that it is possible to re-process the related structure. The internal RF reflector allows for such an action.
3-chokes chamber
DRAWING

## Slide 20: - 60 db Directional Coupler
RF UHV FLANGES
RF AIR FLANGES
AIR WG
VACUUM WG
CLAMPING
133
215
74
CONTACT

## Slide 21: Compact RF Pumping Port
RF INTERFACE FLANGE
TAPERS
VACUUM PORT (CF FLANGE)
serves the needs to pump long waveguide systems to provide the necessary UHV conditions.
consists of two cavities, each made of two oxygen-free copper halves.
cavities are brazed to the stainless steel cylindrical body containing the vacuum port.
pumping interface is the ultra-high vacuum CF flange.
RF network interfaces are WR90 RF vacuum flanges (SLAC or CLIC design).
RF- design

## Slide 22: RF Vacuum Gate Valve
RF-Design
VACUUM GATE VALVE
TAPERS (REMOVABLE)
RF INTERFACE (x2)
Taper (left) assembly
Taper (right) assembly
Gate Valve
allows 100 MW RF power transmission through
used to avoid a ventilation of the whole system during maintenance or replacement of the devices
RF cavities consist of two halves made of oxygen-free copper
vacuum interconnections between valve and cavities are performed by ultra-high vacuum CF flanges
RF network interfaces are WR90 RF vacuum flanges (SLAC or CLIC design)

## Slide 23: Choke Mode Flange
In CLIC the important requirement is the need for independent transverse alignment (of about ±0.1 mm) of the two linacs during machine operation. To avoid the mechanical stresses in a waveguide network we suggested using the double-sector choke-mode flange. This device allows for the electrically contact-free connection between the waveguides and possibility to align transversally the two waveguides without introducing any RF phase errors. The prototype of such a device is now under engineering design optimization.
from
PETS
to AS
double-sector
choke flange

## Slide 24: Hybrid
AS 1
COMPACT
LOAD
AS 2
from
PETS

## Slide 25: Splitter

## Slide 26: Qualification process at CERN

## Slide 27: ACKNOWLEDGEMENT
Many thanks to all
“CLIC Module Working Group”
members at CERN for their contribution !

## Slide 28
Thank you all
for your attention!

## Slide 29: BACKUP MAIN BEAM QUADRUPOLE
MBQ Type 4 prototype assembly
CLIC MB Quad. Main parameters
MBQ Type 1
prototype
under tests

## Slide 30: BACKUP MAIN BEAM QUADRUPOLE

## Slide 31: BACKUP MODULE TYPES
+ special modules (damping region, modules with instrumentation and/or vacuum equipment)
Standard Module (L = 2010 mm)
Drive Beam (100 A)
4 PETS, 2 Quads with BPM
Each PETS feeds 2 AS
Main Beam (1 A)
8 acc. structures
MB filling factor: 91%
Standard Module
73 %
Module Type 2
12 %
Module Type 3
9 %
Module Type 4
3 %
CLIC Module Type1
(3 %)
1 pair of AS replaced by MB Quadrupole

## Slide 32: BACKUP AS
BACK
TO
SLIDE 7

## Slide 33: BACKUP PETS OCTANT
BACK
TO
SLIDE 11

## Slide 34: BACKUP “On-Off” 3-chokes chamber
BACK
TO
SLIDE 18